## Slide 1: The Apollo Guidance Computer
Rory Braybrook
@rbrayb

## Slide 2: Spoiler Alert
Media !!!

## Slide 3: The beginning

## Slide 4: Sputnik - 4 October 1957

## Slide 5: Sputnik - 4 October 1957

## Slide 6: Flopnik - December 6, 1957

## Slide 7: Alan Shepherd - May 5, 1961

## Slide 8: JFK - Address to Congress - May 25, 1961

## Slide 9: We need a computer The “state” of the PC

## Slide 10: Altair 8800 - 1974

## Slide 11: Apple 1 - 1976

## Slide 12: TRS 80 - 1977

## Slide 13: IBM PC - 1981

## Slide 14: NASA mainframe - 1960

## Slide 15: MIT

## Slide 16: Charles Draper lab
MIT chosen because they developed the guidance system for the Polaris missile.
MIT contract with NASA – “develop a navigation, control, and guidance system that would be carried by both the Apollo command module and the lunar lander”.
No detailed requirements.

## Slide 17: The AGC

## Slide 24: Weaving the rope

## Slide 26: AGC stats
5 interrupts
1 Mhz clock
16 bit words
2048 words RAM
36K words ROM (with banked memory)
17 registers
Weighs 70 lbs
Draws 55 watts
First to use IC (Fairchild)
A full decade prior to the first commercially available microprocessor – the 4-bit Intel 4004 central processing unit (CPU) was released in 1971

## Slide 27: Words
Words were 16 bits long - used to represent either data or instructions
Only 15 bits are actually usable (the 16th bit is a parity bit for error checking)
First three bits store an operation code (or “opcode”)
Remaining 12 bits to store an address.
Three bits for the opcode = eight opcodes.
Could sometimes use the fourth bit as part of the op code as well (this required calling an EXTEND instruction first, so the computer would know the following instruction had a special four-bit opcode).

## Slide 28: “OS”
Exec - managed jobs based on priority.
Could run up to eight tasks at a time with each task periodically checking back with the Exec to see if a task with a higher priority was waiting to run.
The Waitlist held tasks waiting for the Exec to have capacity to run them.
Restart parameters (current state) were saved periodically – allowed for restart not reset.

## Slide 29: Interpreter
The AGC provided for manipulation of single- and double-precision quantities
But it needed to handle multi-precision quantities, trigonometric operations, vector and matrix operations, and extensive scalar operations.
"Interpreter" - a “VM”.

## Slide 30: Core sets and VAC
Core sets were the basic task control blocks, including each task's entry point, priority, flags, some memory for temporary variables, and a few other things. (1202)
Interpreted tasks needed more than the 7 words of temporary variables provided by the core sets, so they allocated these VAC (Vector Accumulator) areas for more storage. (1201)

## Slide 31: Dsky

## Slide 35: Nouns and verbs

## Slide 36
# THE FOLLOWING QUOTATION IS PROVIDED THROUGH THE COURTESY OF THE AUTHORS.
#
# "IT WILL BE PROVED TO THY FACE THAT THOU HAST MEN ABOUT THEE THAT
# USUALLY TALK OF A NOUN AND A VERB, AND SUCH ABOMINABLE WORDS AS NO
# CHRISTIAN EAR CAN ENDURE TO HEAR.“
Henry VI, Part 2, Act 4

## Slide 37: Verbs
50 PLEASE PERFORM
51 PLEASE MARK
53 PLEASE MARK ALT LOG
54 REND COAS MARK
56 TERMINATE P20
58 STICKFLAG (R) V50N18 FLAG(S)
64 OPTICS ANGLE TRANSFORM
76 ENABLE VHF DATA PROC

## Slide 38: Nouns
04 ATT ERR
05 ANG SEP ERR-ANG SEP
06 OPTION CODE
09 ALARM CODES
11 TIG NCC
13 TIG NSR
14 STAR TRKR 06.16
18 AUTO MN VR

## Slide 39: Combinations
Verb 37 Enter 63 Enter
V37 = Select Program
63 = sub program (P63)
Verb 5 Noun 9 Enter
Display program alarm codes (1202 / 1201)

## Slide 40: Building the software

## Slide 41: AGC utilities
It didn’t have any that ran on the device
No text editor
No assembler / compiler
No linker

## Slide 42: Cross-compiler
A cross compiler is a compiler capable of creating executable code for a platform other than the one on which the compiler is running.
For example, a compiler that runs on a Windows 7 PC but generates code that runs on Android smartphone is a cross compiler.

## Slide 43: Process
Assemble the program to machine code – oops – not enough mainframe memory!
Compile 20% of the program – write output to file on tape A
Compile next 20% of the program – write output to file on tape A
…
Read the five output files on tape A and concatenate to one file on tape B
Read the machine code from tape B, convert to binary and create the rope instructions

## Slide 44: The types of code
Assembler - ADS LOCCTR
Machine code - 06 1200 Assume 06 is CPU code for ADS
Assume LOCCTR at address 1200
Binary - 110 0 0001 0010 0000

## Slide 45: 1202 Alarm
NEXTCORE CAF COREINC # “Clear and add fixed” – move *COREINC into # accumulator
ADS LOCCTR # “Add to storage” – add accumulator to *LOCCTR
CCS EXECTEM2 # “Count, Compare and Skip”
TCF NOVAC3 # EXECTEM2 > 0 – “Transfer control to fixed”
TC BAILOUT # = 0 - NO CORE SETS “Transfer control” – Call # BAILOUT
OCT 1202 # < 0 – Octal number?

## Slide 46: Interpreter
In particular, the interpretive language used 7-bit opcodes and 15-bit address fields, using the following packed instruction format:
In other words, they packed two instructions in three words.

## Slide 47: Interpreter code
FLAGORGY TC INTPRET # DIONYSIAN FLAG WAVING CLEAR CLEAR NOTHROTL REDFLAG CLEAR SET LRBYPASS MUNFLAG CLEAR CLEAR P25FLAG # TERMINATE P25 IF IT IS RUNNING. RNDVZFLG # TERMINATE P20 IF IT IS RUNNING
(Dionysus is the god of the grape harvest, winemaking and wine, of ritual madness, fertility, theatre and religious ecstasy)

## Slide 48
CLEAR NOTHROTL: “Permit full throttle”
CLEAR REDFLAG: “Landing site redesignation not permitted”
CLEAR LRBYPASS: “Do not bypass landing radar updates”
SET MUNFLAG: “Servicer calls MUNRVG” (MUNRVG is a subroutine that performs some computations needed by the thrusting program)
CLEAR P25FLAG: “P25 not operating” CLEAR RNDVZFLG: “P20 not running” P20 and P25 are programs used during the rendezvous between the command module and the lunar module.

## Slide 49: How to be a developer – circa 1960!

## Slide 52: Punched card

## Slide 53: IBM card punch

## Slide 54: IBM card reader

## Slide 56: Punch card deck

## Slide 58: The mission

## Slide 68: Mission Control

## Slide 71: The players – Kranz, Bales, Garman, Duke

## Slide 72: Apollo 11

## Slide 73: 1202 alarm

## Slide 74: 1201 alarm

## Slide 75: The Eagle has landed

## Slide 77: Apollo 14

## Slide 78: The abort switch
Had roughly 90 minutes – fuel, oxygen, the sun.
Code, test, simulate, upload.
E.g. Verb 21 Noun 1 Enter 1010 Enter 107 Enter
Sets mode register to 71 = Abort in progress
Verb 21 Noun 1 = Load full word
1010 = Address of flags register
107 = Turn abort bit on
65 keystrokes

## Slide 79: The “end”

## Slide 80: The legacy
Only 75 Apollo Guidance computers were ever made, and on average, they each cost the United States around $200,000 (equivalent to $1.5 million today).
The AGC helped 12 men to land on the moon and return safely to earth
It played a major role in the safe recovery of Apollo 13
It never crashed!

## Slide 81: December 14th 1972 – Apollo 17 blasts off from the moon
The last lunar mission
Sadly, we have never been back

## Slide 82: References
Sunburst and Luminary – An Apollo Memoir – Don Eyles
The Apollo Guidance Computer – Architecture and Operation – Frank O’Brien
Digital Apollo – Davis A Mindell
Left Brains for the Right Stuff – Hugh Blair-Smith
Virtual AGC – Home Page - http://www.ibiblio.org/apollo/
Original Apollo 11 Guidance Computer (AGC) source code for the command and lunar modules - https://github.com/chrislgarry/Apollo-11